## Slide 1: Lecture 1.1: Introduction

## Slide 2: Agenda
1
What is Firewall
Types of Firewall
2
Firewall in Linux kernel
3
Notes: 2
2
2

## Slide 3: What is Firewall
1
What is Firewall
Types of Firewall
2
Firewall in Linux kernel
3
Notes: 3
3
3

## Slide 4: What is Firewall
Primary goal: protect an internal network (or host) from external attacks
Inspects and controls network traffic
Controls the incoming and outgoing network traffic from a network (or host) based on a rule set
A firewall establishes a barrier between a trusted, secure internal network and another network (e.g., the Internet) that is not assumed to be secure and trusted
Can be hardware or software-based, depends on needs

## Slide 5: Network topology
All network traffic should go though the firewall to be effective
We need to set up the network topology in such way that all incoming/outgoing traffic will go though the firewall

## Slide 6: Uses of firewall
Barrier between a trusted network to the world
Enforce protocol correctness
Enforce policy of the network administrator
Minimize chance of intrusion & attacks
Can operate in different levels of the network stack:
  First firewalls looked up to the TCP/IP level
  Today’s firewalls inspect all the way up to the application level

## Slide 7: Firewall’s capabilities and implementation goals
Implementation goals:
  Should have minimum performance impact on the network
  Easy to configure
  Provide the user information (logging or monitor system)
Limitations:
  Cannot inspect packets which bypass the firewall
  Internal threats usually don’t get inspected by the firewall
  Virus-infected files and programs are transparent to the firewall

## Slide 8: How does Firewall works
1
What is Firewall
Types of Firewall
2
Firewall in Linux kernel
3
Notes: 8
8
8

## Slide 9: Types of Firewall (chronological order)
Static packet filtering gateway
  Stateless packet filtering/inspection
Circuit-level Gateway
Application-level/proxy gateway
Dynamic packet filtering gateway
  Stateful inspection

## Slide 10: But first, OSI and TCP/IP models
The OSI and TCP/IP models

## Slide 11: TCP/IP
We need to get two applications situated in remote hosts to communicate
We have a standard model that divides the communication functionality to separated abstraction layers
Each layer implementation is hidden from other layers implementation
Each layer has a protocol family which governs the way information is passed by it
We will be interested mostly in layers 3 and 4, and the data itself

## Slide 12: Layer 3 (network layer)
In TCP/IP, each host has an address, which is called IP address
In IPv4 the address has the form X1 . X2 . X3 . X4:
  Each of these four fields ranged from 0 to 255 (1 byte)
When a host tries to connect to remote host, he sands its address as an information for the destination and the gateways on the way
A router, or gateway, forwards traffic from one network to another
  It use its routing table to know where the destination host is
  If he doesn’t know – he moves it to the default gateway

## Slide 13: Layer 4 (Transport layer)
On each host there is an application. Both applications need to pass data between them.
  Need to make sure the data gets to the applications in the order it was send
  Needs to make sure the data gets to the correct destination.
We have a TCP protocol family to make sure it happens.
  For every chunk of data received the sending host needs to be informed
  To start sending data, there got to be a connection
  When no more data needs to be send the connection must be closed

## Slide 14: Layer 4 (Transport layer) – establishing a connection
To initiate a TCP connection, we have a 3-way handshake:
  SYN + seq(X)
    “Hello, I’m here. I chose X.”
  SYN + seq(Y) + ACK + ack(X+1)
    “I heard your X. here’s your X+1. I’m here too, I chose Y.”
  ACK + ack(Y+1)
    “I heard your Y, here’s your Y+1.”
Now a connection has been established

## Slide 15: Layer 4 (Transport layer) – passing data
Now that we have a connection we can start sending data
On each host every application has a port number
When a packet arrives to the host it moves the data to the process that is associated with that port
Server usually have a publicly known port numbers
  HTTP:80
  HTTPS:443
  SSH:22
Clients usually have higher numbers that changes between every TCP connection

## Slide 16: Layer 4 (Transport layer) – passing data (continues)
Each side sends data to the other side
The data is chunked over segments
The side that sends the packets wait for a conformation
After it receives ACK it continues to send data
In any case of data getting lost, we can ask for retransmission

## Slide 17: Layer 4 (Transport layer) – terminating a connection
To terminate a connection:
  FIN (client)
    “I want to end this conversation”
  ACK + FIN(server)
    “ok, just let me finish…I’m done”
  ACK (client)
    “bye bye”

## Slide 18: A packet’s journey
The tcp/ip stack
Logical transfer
physical transfer

## Slide 19: Stateless packet filtering
Works by a static rule table
Each packet is individual
Works on the transport and network layers
Checks only the interesting header fields and compare them with the rules, doesn't look in the packet’s data
Each packet that is inspected waits for a verdict - accept or drop

## Slide 20: IP header (network layer)
We need to see the source and destination IP addresses to determine if accept or deny the packet

## Slide 21: TCP header (transport layer)
We want to know the source and destination ports, and the SYN/ACK flags to determine if accept or deny the packet

## Slide 22: Stateless packet filtering
Rule for example
  We’re not allowing incoming network designated to port 80
Direction | Src address | Dst address | Protocol | Src port | Dst port | Syn/Ack | Action
In | Any | Network | any | any | 80 | Any | deny

## Slide 23: Stateless inspection
Pros
Low performance impact
Easy to configure
Cons
Relies on static header fields, therefore easy to spoof and manipulate
Doesn’t look in the data itself
Transparent to the client

## Slide 24: Circuit-level Gateway
Monitor TCP handshake between packets to determine if the session request is legitimate. Saves connections in dynamic connection tables
Create 2 TCP connection, functions as MITM
Works on the session layer

## Slide 25: Circuit-level Gateway
Pros
Low performance impact
conceal the network itself from the external computer
Cons
Doesn’t filter individual packets, after legitimate session opening doesn’t check what’s coming
Transparent to the client
Handle only TCP connections

## Slide 26: Application-level/proxy gateway
[Restricted] ONLY for designated groups and individuals
Sits in the middle of the service and operate as a server (to the client) and as a client (to the server)
Hence – a proxy server, filter and examine individual packets streams, depends on the service/application
Works on the application layer

## Slide 27: Application-level/proxy gateway
Pros
Inner hosts IP hiding
Header destruction
Cons
High performance impact (data based filter, not only specific fields from headers)
Protocol enforcement
logging
Not transparent to the client
Only supported protocols can be used

## Slide 28: Stateful inspection
[Restricted] ONLY for designated groups and individuals
Decide what to do with a packet based on:
Dynamic connection tables
Old connections
Information from the application layer
Combination of all older methods
Inspect the headers and the data

## Slide 29: Stateful inspection
Pros
Good security coverage, deals with all levels and able to provide high level of defense
Cons
Complicated and can hurt security and experience if not managed properly
No proxies – transparent to the client
Most expansive method (requires most resources)

## Slide 30: Types of Firewall
1
What is Firewall
Types of Firewall
2
Firewall in Linux kernel
3
Notes: 30
30
30

## Slide 31: Packet inspection in Linux kernel
As we discus, the firewall should have minimum performance impact. Therefore we need to implement it in the kernel, so it would have access to Linux network structures to be able to see the packets.
Linux use structure for each protocol and layer
We will be interested in the internet and transport layer (and of course the data itself)
Data
HTTP/1.1 200 OK0x20Last-Modified: Mon, 07 Apr 2014 09:16:25
GMT0x20Content-Type: image/jpeg0x20Cache-Control:
max-age = 3153600000x20magicmarker: 10x20Content-Length:
47060x20Accept-Ranges: bytes0x20Date: Mon, 07 Apr 2014
11:35:46 GMT0x20X-Varnish: 2786274250 27578957660x20Age:
IP header
TCP/UDP header

## Slide 32: Lecture 1.2: Linux and Networking

## Slide 33: Agenda
1
Linux kernel modules and networking
Netfilter
2
About first Assignment
3
4
Virtualization
Notes: 33
33
33

## Slide 34: Virtualization
1
Virtualization
Netfilter
2
3
Linux kernel modules and networking
About first Assignment
4
Notes: 34
34
34

## Slide 35: Virtual network
Virtual Machine software, like VMware or VirtualBox, provide a service which allow us to build not only virtual computers, but virtual networks too.

## Slide 36: The Virtual NIC
Although we only have one NIC, we can
simulate multiple NICs
vNICs send and receive data through
the physical NIC
Data is written to register-variables, sent to the
physical registers
When an answer arrived the NIC interrupts,
the virtualization layer inject the interrupt into the vNIC
Virtualization layer

## Slide 37: Virtual Network in our Workshop
in
out

## Slide 38: The VMs
There are three virtual machines we will work with:
  FW: this is the firewall machine, which will sit in the middle of the topology. It runs Ubuntu with GUI, so you can do development inside the VM
in
out

## Slide 39: The VMs
There are three virtual machines in the course site:
  2-3. host1 and host2: testing machines which will communicate with each other though your firewall. Runs Ubuntu cli
in
out

## Slide 40: Linux kernel modules and networking
1
Virtualization
Linux kernel modules and networking
2
Netfilter
3
About first Assignment
4
Notes: 40
40
40

## Slide 41: What is a Kernel Module
An object file that contains code to extend the operating system’s kernel
Loaded at run time, after kernel is already up and running
Adds functionality:
  Device drivers
  New features

## Slide 42: How kernel modules different from user-space programs
Cannot use regular libraries, like stdlib
  Most of C library is implemented in the kernel
  Besides, <kernel.h> offers some nice utilities
Cannot use floating point math
Run in privileged mode, so security is critical
  Don’t trust the user
  Check all input sizes, formats, etc.
  Check all exceptional conditions and potential errors
  Don’t trust the user
More about it - Linux Kernel Development, pages 16-22

## Slide 43: Building the Module
The purpose – eliminate the need to re-compile the kernel every time you need to add/remove a specific feature
A Makefile that adapts itself to current kernel
Put the module in and out the kernel by command line
  insmod <module name> to insert the module
  rmmod <module name> to remove it
Initialization function that is called when the module enters the kernel
Cleanup function that is called when the module is removed from the kernel

## Slide 44: Simple kernel module
#include <linux/module.h> /* Needed by all modules */
#include <linux/kernel.h> /* Needed for KERN_INFO */
int init_module(void) {
printk(KERN_INFO "Hello World!\n");
return 0; /* if non-0 return means init_module failed */
}
void cleanup_module(void) {
printk(KERN_INFO "Goodbye World!\n");
}

## Slide 45: Explanation
init_module() is called when module is loaded
cleanup_module() is called when module is unloaded
Another option: Macros!

## Slide 46: Simple module with macros
#include <linux/module.h> /* Needed by all modules */
#include <linux/kernel.h> /* Needed for KERN_INFO and for the Macros */
static int __init my_module_init_function(void) {
printk(KERN_INFO "Hello World!\n");
return 0; /* if non-0 return means init_module failed */
}
static void __exit my_module_exit_function(void) {
printk(KERN_INFO "Goodbye World!\n");
}
module_init(my_module_init_function);
module_exit(my_module_exit_function);

## Slide 47: What are Macros and why
__init and __exit macros tells the kernel when we use those functions
This allows to free kernel memory that is used only at init
  Kernel memory is scarce, and we need to free it whenever we can

## Slide 48: How to compile a Linux module?
Suppose that our simple module called “module.c”
We need in this folder another file called “Makefile” (case sensitive)
This file contains instructions to the OS how to compile this module

## Slide 49: Simple Makefile
obj-m += module.o
all:
make -C /lib/modules/$(shell uname -r)/build M=$(PWD) modules
clean:
make -C /lib/modules/$(shell uname -r)/build M=$(PWD) clean

## Slide 50: How to compile a Linux module?
Then, the command “make” compiles the module
The file “module.ko” is the executable file

## Slide 51: How to load a Linux module?
The command “insmod <mod_name>.ko” binds the module to the kernel. The “init” function is being execute
The command “rmmod <mod_name>” removes the module from the kernel. The “cleanup” function is being execute

## Slide 52: Our Kernel Module – The Firewall!
What will we do with our kernel module? (spoilers ahead)
  Register our own functions (AKA: hooks) with the netfilter API, to issue verdicts on packets going in/out/through our Linux box
  Register a char device, to communicate with the user space
    Send commands to set module values
    Receive data from the firewall about the state of the system
When our module will be removed, it will clean up all this mess, as if it was never there

## Slide 53: Linux networking
We need a way to see the packets
Packets has headers for each layer and data
Linux contains set of useful tools and structures to manage packets over the kernel

## Slide 54
Each packet comes with headers, each for every layer
The layers we are interested in are the network layer and transport layer
Packet Headers
Data
HTTP/1.1 200 OK0x20Last-Modified: Mon, 07 Apr 2014 09:16:25
GMT0x20Content-Type: image/jpeg0x20Cache-Control:
max-age = 3153600000x20magicmarker: 10x20Content-Length:
47060x20Accept-Ranges: bytes0x20Date: Mon, 07 Apr 2014
11:35:46 GMT0x20X-Varnish: 2786274250 27578957660x20Age:
83980x20Via: 1.1 varnish0x20Connection: keep-alive0x20X-Cache:
IP header
TCP/UDP header

## Slide 55
IP Header

## Slide 56
IP Header, how Linux knows it
Declared in linux/ip.h
To be on the safe side, don’t forget to use htonl, htons, ntohl, ntohs when processing the fields

## Slide 57
Data
HTTP/1.1 200 OK0x20Last-Modified: Mon, 07 Apr 2014 09:16:25
GMT0x20Content-Type: image/jpeg0x20Cache-Control:
max-age = 3153600000x20magicmarker: 10x20Content-Length:
47060x20Accept-Ranges: bytes0x20Date: Mon, 07 Apr 2014
11:35:46 GMT0x20X-Varnish: 2786274250 27578957660x20Age:
83980x20Via: 1.1 varnish0x20Connection: keep-alive0x20X-Cache:
IP header
Each packet comes with headers, each for every layer.
The layers we are interested in are the network layer and transport layer
Packet Headers
TCP/UDP header

## Slide 58
Data
HTTP/1.1 200 OK0x20Last-Modified: Mon, 07 Apr 2014 09:16:25
GMT0x20Content-Type: image/jpeg0x20Cache-Control:
max-age = 3153600000x20magicmarker: 10x20Content-Length:
47060x20Accept-Ranges: bytes0x20Date: Mon, 07 Apr 2014
11:35:46 GMT0x20X-Varnish: 2786274250 27578957660x20Age:
83980x20Via: 1.1 varnish0x20Connection: keep-alive0x20X-Cache:
IP header
Each packet comes with headers, each for every layer.
The layers we are interested in are the network layer and transport layer
Packet Headers
TCP/UDP header

## Slide 59
TCP Header

## Slide 60
TCP Header, how Linux knows it
Defined in linux/tcp.h

## Slide 61
UDP Header
Defined in linux/udp.h

## Slide 62
ICMP Header
Defined in linux/icmp.h

## Slide 63
Data
HTTP/1.1 200 OK0x20Last-Modified: Mon, 07 Apr 2014 09:16:25
GMT0x20Content-Type: image/jpeg0x20Cache-Control:
max-age = 3153600000x20magicmarker: 10x20Content-Length:
47060x20Accept-Ranges: bytes0x20Date: Mon, 07 Apr 2014
11:35:46 GMT0x20X-Varnish: 2786274250 27578957660x20Age:
83980x20Via: 1.1 varnish0x20Connection: keep-alive0x20X-Cache:
sk_buff
IP header:
TCP/UDP header
The Linux struct that holds a pointer to the packet and metadata about the packet
Hold many fields for many purposes
  head, data, tail , end
  transport layer headers
    tcphdr, udphdr, icmphdr
  network layer headers
    iph, ipv6h
The packet is copied directly to the RAM (DMA) and each part of the kernel that touches it, just gets a pointer

## Slide 64: Agenda
1
Virtualization
Linux kernel modules and networking
2
Netfilter
3
About first Assignment
4
Notes: 64
64
64

## Slide 65: Netfilter
Easy API to handle and examine packets from the internet
  #include <linux/netfilter.h>
  #include <linux/netfilter_ipv4.h>
Allow us to hook functions to the packet’s route on a specific (important) points though the kernel
There are 5 inspection points we can hook into, each for a different type of packets

## Slide 66: Netfilter hook points
Where packets come in, having passed the simple sanity checks they are passed to the netfilter framework's NF_IP_PRE_ROUTING hook

## Slide 67: Netfilter hook points
The routing code decides whether the packet is destined for another interface or a local process. If it's destined for the box itself, the netfilter framework is called again for the NF_IP_LOCAL_IN hook, before being passed to the process

## Slide 68: Netfilter hook points
If it's destined to pass to another interface instead, the netfilter framework is called for the NF_IP_FORWARD hook

## Slide 69: Netfilter hook points
The packet then passes a final netfilter hook, the NF_IP_POST_ROUTING hook, before the packet reaches the wire again.

## Slide 70: Netfilter hook points
The NF_IP_LOCAL_OUT hook is called for packets that are created locally.
  Routing code is called before this hook to figure out the IP address and after this hook to decide the route.

## Slide 71: Netfilter hook points
You can find it in the source code: https://elixir.bootlin.com/linux/v4.15/source/include/uapi/linux/netfilter_ipv4.h#L44

## Slide 72
The hook

## Slide 73: Agenda
1
Virtualization
Linux kernel modules and networking
2
Netfilter
3
About first Assignment
4
Notes: 73
73
73

## Slide 74: Assignment 1 – Building the virtual lab
In this assignment we will create the virtual lab
Use VirtualBox or VMware workstation.
  Don’t use VMware player, it doesn’t support virtual networks
Pay attention for network configuration (make it persistent)
In the course site you’ll have 3 VMs (for VirtualBox): client, server and FW, so wont have to lose time installing Ubuntu machines. Most of the heavy coding will be performed on the FW VM

## Slide 75: Assignment 1
Make sure you don’t have kernel panics when you load the module – this would have heavy penalty on your grade
In this assignment, you decide the verdict for each packet base on it’s type, not content. Make use of that fact to make it easier on you. That said, you can use whatever method you want